## Slide 1: Meeting Information
This workshop starts at 9:30 a.m.
“Virtual Blue Speaker Card” – To provide oral comments, obtain Zoom Password. Email DDWRegUnit@Waterboards.ca.gov
Written comments can be sent via email to: commentletters@waterboards.ca.gov
Subject line: “Comment Letter – Metal DLRs Workshop“
Comments are due November 18, 2022

## Slide 2: Metals Detection Limit for Purposes of Reporting (DLR)
Pre-rulemaking Workshop
Thursday, November 3, 2022
9:30 a.m.
October 2021

## Slide 3: State Water Boards' Mission Statement To preserve, enhance, and restore the quality of California's water resources and drinking water for the protection of the environment, public health, and all beneficial uses, and to ensure proper water resource allocation and efficient use, for the benefit of present and future generations.

## Slide 4: Meeting Logistics
Meeting is being recorded
Registered Participants will be muted until asked to comment
“Virtual Blue Speaker Card” – Obtain Zoom Password
  Email DDWRegUnit@Waterboards.ca.gov
  Subject line, indicate: Metal DLRs Workshop
  Your name
  Who you represent (i.e., self, another person, an organization)
  Whether you intend to participate via videoconference or telephonically
  If calling in, please provide the last three digits of the phone number you will be calling from

## Slide 5: Today’s Workshop
No action on regulation today
Intent is to receive public comments on metal DLRs
Comments must be submitted by Friday, November 18, 2022, noon
Future opportunities to comment
  45-day public comment period at the start of formal rulemaking process
  Additional comment periods for regulation changes, if needed

## Slide 6: Outline
Brief Background
November 2021: Initial Survey
February 2022: Follow-Up
Regulatory Proposal
Inform the public and interested parties about the proposed metals detection limits for purposes of reporting (DLRs)
Collect the public’s feedback before the official rulemaking process starts

## Slide 7: Definition of Key Terms

## Slide 8: "Detection Limit for Purposes of Reporting (DLR)"
Detection Limit for Purposes of Reporting (DLR)
  “Designated minimum level at or above which any analytical finding of a contaminant in drinking water resulting from monitoring must be reported to the State Water Board”
  [22 Cal. Code of Regs section 64400.34]
Detection Limit for Purposes of Reporting (DLR)
  The designated minimum level at or above which any analytical finding of a contaminant in drinking water resulting from monitoring required under this chapter shall be reported to the Department.
  [22 Cal. Code of Regs section 64671.15]
Part of criteria for reduced tap sampling frequency [section 64676.5]
Part of criteria for reduced water quality parameter (WQP) sampling, corrosion control [section 64674]

## Slide 9: Primary and Secondary Drinking Water Standards
Primary drinking water standard (HSC 116275)
  Maximum level of a contaminant (MCLs) that have adverse effect of health
  Specific treatment techniques adopted in lieu of MCLs
  Monitoring and reporting requirements for MCLs
  e.g., MCLs, Lead and Copper Rule action levels
Secondary drinking water standards (HSC 116275)
  Aesthetic impacts (taste, color, odor)
  e.g., Secondary MCLs [22 Cal. Code of Regs section 64449]

## Slide 10: Notification Levels
Health based advisories established by DDW
When chemicals are found at concentrations greater than their NLs, certain requirements and recommendations apply
Response Levels (RLs)
  Depends on NL toxicological endpoint basis
  If chemicals present exceed the RL, DDW recommends source be taken out of service
  For PFAS compound NLs, additional requirements per state law
  e.g., Manganese NL (500 µg/L), PFHxS NL (3 ng/L)

## Slide 11: Public Health Goal (PHG)
Public Health Goal (PHG) for contaminants set by Office of Environmental Health Hazard Assessment (OEHHA)
Level of a contaminant in drinking water below which there is no known or expected risk to human health
Non-enforceable

## Slide 12: Relationship Between MCL, DLR, and PHG
*Several contaminant MCLs are lower then their respective PHGs
MCL
Drinking water standard
DLR
DLR
PHG
Level of a contaminant in drinking water below which there is no known or expected risk to human health
DLR
DLRs above the PHG limit ability to evaluate technological feasibility of MCL revision and whether technology can achieve greater health protection
DLR
Minimum level at which finding must be reported

## Slide 13: How is the level of an MCL determined?
Step 1: What level can we measure to?
Step 2: What level can we treat to?
Step 3: What treatment level can we pay for?
Technological Feasibility
Economic Feasibility

## Slide 14: Technological Feasibility
Health and Safety Code section 116365 – set MCL as close to the PHG as technologically and economically feasible
Analytical methods able to detect to at least at the proposed DLR while maintaining target spike recovery range
Adequate laboratory capacity available
  e.g., How many laboratory can achieve the proposed DLR? What is their volume of samples analyzed statewide? Where are the laboratories located?

## Slide 15: Metals Summary
Contaminant | MCL (µg/L) | DLR (µg/L) | PHG (µg/L)
Arsenic | 10 | 2 | 0.004
Antimony | 6 | 6 | 1
Beryllium | 4 | 1 | 1
Cadmium | 5 | 1 | 0.04
Mercury | 2 | 1 | 1.2
Nickel | 100 | 10 | 12
Thallium | 2 | 1 | 0.1
Lead * | 15 | 5 | 0.2
Iron ** | 300 | NA | NA
Manganese ** | 50 | NA | NA
Zinc ** | 5000 | NA | NA
* Action level for lead under Lead and Copper Rule.
** Secondary MCLs for Iron, Manganese, and Zinc. Manganese has a notification level of 500 µg/L.
µg/L = micrograms per liter, equivalent to parts per billion (ppb)

## Slide 16: Brief Summary of Proposal
Phase I
Lower lead and nickel DLRs
Adopt DLRs for contaminants with secondary MCLs
Correction of uranium DLR to reflect unit conversion from mg/L to pCi/L
Phase II
Three-year compliance schedule
Lower arsenic, antimony, beryllium, cadmium, mercury, and thallium DLRs
Further lower the lead and manganese DLRs adopted in Phase I

## Slide 17: Summary of Laboratory Surveys

## Slide 18: November 2021 Initial Survey
53 accredited laboratories surveyed that submitted drinking water quality data within the last 5 years
21 responses over 3 weeks:
  12 commercial laboratories; 9 municipal laboratories
Laboratories asked to identify minimum reporting level (MRL), lowest calibration point, current analysis costs, projected cost increases for a specified MRL, and more
Map of Responding Laboratories

## Slide 19: Initial Survey: MRLs of Metals with Primary Drinking Water Standard
MRL (µg/L) | Antimony | Arsenic | Beryllium | Cadmium | Lead | Mercury | Nickel | Thallium
PHG | 1 | 0.004 | 1 | 0.04 | 0.2 | 1.2 | 12 | 0.1
25th percentile | 0.5 | 0.5 | 0.5 | 0.2 | 0.5 | 0.1 | 1 | 0.2
50th percentile | 1 | 1 | 0.5 | 0.5 | 0.5 | 0.2 | 2 | 0.8
75th percentile | 1 | 2 | 1 | 1 | 1 | 1 | 5 | 1
Responses (N) | N = 18 | N = 19 | N = 22 | N = 20 | N = 18 | N = 18 | N = 21 | N = 18
Contaminant | Antimony | Arsenic | Beryllium | Cadmium ​ | Lead ​ | Mercury ​ | Nickel ​ | Thallium ​
Current DLR (µg/L) ​ | 6 | 2 | 1 | 1 | 5 | 1 | 10 | 1 ​
MRL = Minimum Reporting Level.

## Slide 20: Initial Survey: MRL for Metals with Secondary MCLs
MRL (µg/L) | Iron | Manganese | Zinc
25th percentile | 23 | 1 | 5
50th percentile | 30 | 5 | 10
75th percentile | 50 | 16 | 35
90th percentile | 100 | 20 | 50
Responses (N) | N = 19 | N = 24 | N = 24
Contaminant | Iron​ | Manganese​ | Zinc​
Secondary MCL (µg/L)​ | 300 | 50 | 5000
MRL = Minimum Reporting Level.

## Slide 21: Initial Survey: Current Sample Analysis Costs
Analytical Method | Single/Suite | Average Cost | Median Cost
EPA Method 200.7 | Single | $38 | $40
EPA Method 200.7 | Suite | $23/analyte | $21/analyte
EPA Method 200.8 | Single | $32 | $30
EPA Method 200.8 | Suite | $29/analyte | $23/analyte
SM 3113B | Single | $40 | $40
EPA Method 245.1 (Mercury only) | Single | $71 | $60
Range of average costs
Single element analysis: $32 to $71
Single analyte, if performed in a suite: $23 to $29
Analyses performed in suite generally lower in cost per analyte

## Slide 22: Initial Survey: Projected Cost Increase Based on Target MRL
Survey proposed a target MRL to assess current technological capabilities
  10 times or 100 times lower than established DLR or MCL
Summary of responses:
50%+ of responding laboratories indicated a 20%+ increase in cost
~19 to 47% indicated the need to purchase new equipment to achieve the target MRL
$25,000 to $400,000 for equipment depending on analyte and analytical method used

## Slide 23: February 2022 Follow-up Survey
Sent to labs that responded to initial survey
New target DLRs based on initial survey responses
In the survey, laboratories
Rated ability to achieve lowered DLR on a scale of 1 (impossible) to 5 (can do now)
Reported cost impact as a percent increase of current analysis costs (individual or suite)
Provided input on what it would take to achieve a lower DLR than the proposed DLRs
Notes: Rank Icon Source
Coin Icon Source
Survey Icon Link

## Slide 24: Follow-up Survey: Costs
Range of percent cost increases for proposed metal DLR (minimum and maximum)
Proposed DLR | Number of Labs | Arsenic | Cadmium | Lead | Mercury | Nickel | Thallium | Iron | Manganese | Zinc
Analytical Method | C = Commercial M = Municipal | 1 µg/L* | 0.5 µg/L* | 0.5 µg/L* | 0.2 µg/L* | 2 µg/L* | 0.8 µg/L* | 100 µg/L | 20 µg/L | 50 µg/L
EPA 200.7 | C = 2, M = 4 | - | 0 to 20% | - | - | 0 to 43% | - | 0% | 0% | 0%
EPA 200.8 | C = 4, M = 9 | 0 to 20% | 0 to 20% | 0 to 20% | 0 to 20% | 0% | 0 to 20% | 0% | 0% | 0%
SM 3113B | C = 0, M = 1 | 45% | - | 45% | - | - | - | - | - | -
EPA 245.1 | C = 3, M = 2 | - | - | - | 0 to 40% | - | - | - | - | -
Number of labs indicate how many commercial (C) and municipal (M) use the analytical method.
* (Asterisk) indicates proposed DLR with a 3-year implementation period.

## Slide 25: Follow-up Survey: Laboratory Capability
Chart: 
| Pb = 0.5 ug/L | Ni = 2 ug/L | As = 1 ug/L | Cd = 0.5 ug/L | Hg = 0.2 ug/L | Tl = 0.8 ug/L
Impossible | 2 | 2 | 1 | 1 | 1 | 1
Very unlikely | 0 | 0 | 0 | 0 | 0 | 0
Possible | 2 | 1 | 3 | 1 | 3 | 2
Very likely | 3 | 0 | 1 | 1 | 3 | 2
Can do now | 4 | 7 | 5 | 6 | 3 | 4
N = 14
Results of laboratory ability to achieve specified lower DLR given 3 years to develop adequate capacity.
N = 14
N = 14
N = 14
N = 11
N = 12

## Slide 26: Follow-up Survey: Lower DLRs
Contaminant | Arsenic | Cadmium | Lead | Mercury | Nickel | Thallium
Target DLR | 0.5 µg/L | 0.1 µg/L | 0.2 µg/L | 0.1 µg/L | 1 µg/L | 0.1 µg/L
Key Findings
Several commercial and municipal laboratories reported an arsenic DLR of 0.5 ug/L is possible now using EPA 200.8
For other metals, laboratories indicated the need
  For new equipment, method development, and staff training
  For refining method detection limit or lower calibration
  To eliminate trace levels of analytes in background

## Slide 27: Regulatory Proposal

## Slide 28: Regulatory Proposal – Revised Primary MCL DLRs
Contaminant | Revised DLR (mg/L) | Revised DLR (ug/L)
Arsenic | 0.0005* | 0.5*
Antimony | 0.001* | 1*
Beryllium | 0.0005* | 0.5*
Cadmium | 0.0005* | 0.5*
Mercury | 0.0002* | 0.2*
Nickel | 0.005 | 5
Thallium | 0.0008* | 0.8*
*Effective three years after regulation takes effect.

## Slide 29: Regulatory Proposal – Adoption of Secondary MCL DLRs
Establishing DLRs for constituents with secondary MCLs
Constituent | Proposed DLR (mg/L) | Proposed DLR (ug/L)
Iron | 0.1 | 100
Manganese | 0.02 0.01* | 20 10*
Zinc | 0.05 | 50
*Effective three years after regulation takes effect.

## Slide 30: Regulatory Proposal – Revised Lead DLR
Contaminant | Proposed DLR (mg/L) | Revised DLR (ug/L)
Lead | 0.001 0.0005* | 1 0.5*
*Effective three years after regulation takes effect.
Revisions to reduced monitoring frequency criteria such that the criteria does not use the proposed lowered DLRs

## Slide 31: Regulatory Proposal – Radionuclides DLR
Correction of uranium DLR to reflect the unit conversion from µg/L to pCi/L
  Federal uranium detection limit is 1 µg/L
  Current CA uranium DLR is 1 pCi/L, which is equivalent to 1.48 µg/L
  Proposed uranium DLR is 0.68 µg/L

## Slide 32: Summary of Regulatory Proposal
Contaminant | PHG (mg/L) | Standard (mg/L) | Current DLR (mg/L) | Proposed Phase I DLR (mg/L) | Proposed Phase II DLR (mg/L)
Antimony | 0.001 | 0.006 | 0.006 | No change | 0.001
Arsenic | 0.000004 | 0.010 | 0.002 | No change | 0.00050
Beryllium | 0.001 | 0.004 | 0.001 | No change | 0.0005
Cadmium | 0.00004 | 0.005 | 0.001 | No change | 0.0005
Iron | None | 0.3 | None | 0.10 | No change
Lead | 0.0002 | 0.015 | 0.005 | 0.001 | 0.0005
Manganese | None | 0.05 | None | 0.02 | 0.01
Mercury | 0.0012 | 0.002 | 0.001 | No change | 0.0002
Nickel | 0.012 | 0.1 | 0.01 | 0.005 | No change
Thallium | 0.0001 | 0.002 | 0.001 | No change | 0.0008
Zinc | None | 5.0 | None | 0.05 | No change

## Slide 33: Comments
California Water Boards

## Slide 34: Participation Instructions
Webcast Participants
video.calepa.ca.gov
Registered Participants will be muted until asked to comment
“Virtual Blue Speaker Card” – Obtain Zoom Password
  Email DDWRegUnit@Waterboards.ca.gov
  Subject line, indicate: Metal DLRs Workshop
  Your name
  Who you represent (i.e., self, another person, an organization)
  Whether you intend to participate via videoconference or telephonically
  If calling in, please provide the last three digits of the phone number you will be calling from

## Slide 35: Comments on the Proposal
Comments should be related to the regulatory proposal outlined in this presentation
In addition, feedback on ways to improve laboratory survey and participation is welcomed.
All comments may be made public

## Slide 36: Submitting Written Comments
Public Comments deadline November 18, 2022, noon.
  Written comments can be sent via email to:
  commentletters@waterboards.ca.gov
  Subject line: “Comment Letter – Metal DLRs Workshop"
  All comments may be made public

## Slide 37: Thank You
Public Comments before November 18, 2022, noon.
  Drinking Water Rulemaking Questions
  melissa.hall@waterboards.ca.gov
Email List – Drinking Water Program Announcements:
bit.ly/SWRCB_Email_SignUp