## Slide 1
Item #17: Board Workshop
Alamitos Bay and Los Cerritos Channel
Watershed Management Area
Watershed Management
Program Approach October 9, 2014

## Slide 2
Unincorporated
County Island
Located in Los Cerritos Channel Watershed
Landlocked by the City of Long Beach
95 acres
Los Cerritos Channel
San Gabriel River

## Slide 3
Unincorporated County Island
Predominately single family residential neighborhood
3 catch basins

## Slide 4
Water Quality Priorities
County Island
Los Cerritos Channel Metals TMDL
Greater Harbors Toxics TMDL
Waterbody | Category 1 (Highest Priority) |  | Category 2 (High Priority) | Category 3 (Medium Priority) | Low Priority Pollutants
 | Pollutant | TMDL |  |  | 
Los Cerritos Channel | Copper (wet and dry) | LCC Metals | Ammonia | MBAS | Cadmium (wet)
 | Lead | LCC Metals/DC Toxics | Bis(2ethylhexyl) phthalate (DEHP) | Enterococcus | Chlorpyrifos (wet)
 | Zinc | LCC Metals/DC Toxics | Chlordane (Sediment) |  | Chromium (wet)
 | DDT (fish tissue) | DC Toxics | Coliform Bacteria |  | Diazinon (wet and dry)
 | PCBs (fish tissue) | DC Toxics | Trash |  | Dissolved Silver (wet)
 | Chlordane (fish tissue) | DC Toxics | pH |  | 
 | PAHs (sediment) | DC Toxics |  |  | 
 | Toxicity (sediment) | DC Toxics |  |  | 

## Slide 5
Outreach and Stakeholder Input
Partnered with other WMP groups for a Stakeholder Outreach meeting on April 30th, 2014.
Received positive remarks from Stakeholders.

## Slide 6
Pollutant Reduction Strategy
June 28, 2014
WMP/CIMP Submitted
Implement Watershed Control Measures (WCMs)
July 2017
If exceedances are found:
Implement County Island Specific Monitoring
July 2017
In compliance:
Continue implementing previous WCMs and monitoring
July 2015
Monitor 2 Downstream Locations
July 2019
If exceedances are found:
Implement Additional Watershed Control Measures
Final Compliance Dates:
2023: Los Cerritos Channel Metals TMDL- Dry Weather
2026: Los Cerritos Channel Metals TMDL- Wet Weather
2032: Harbors Toxics TMDL
Computer modeling shows a 72% reduction in zinc is needed by 2026

## Slide 7
Non-Storm Water Outfall Based Monitoring
County Island has 4 outfalls into Palos Verde Drain
2 screenings have been conducted so far
No significant flow

## Slide 8
Selected Watershed Control Measures
  Enhanced Street Sweeping
  Vacuum sweepers capture fine sediments that metals are bound to
*Image courtesy of Elgin Sweepers

## Slide 9
Selected Watershed Control Measures
  Full capture devices and automatic retractable screens
  Reduce trash and sediment from entering storm drain system
  Increased catch basin cleanout

## Slide 10
Selected Watershed Control Measures
  Green Streets Policy/Green Infrastructure Guidelines are in place
  Low Impact Development Ordinance is in place

## Slide 11
Potential Watershed Control Measures
  Pervious Catch Basins

## Slide 12
Potential Watershed Control Measures
  Modular Wetlands

## Slide 13
Next Steps
  Implement identified WCMs
  Monitoring efforts have begun
  Evaluate monitoring data
  Implement additional WCMs to meet water quality priorities

## Slide 14
BILL JOHNSON, P.E. Watershed Management Division
County of Los Angeles
Department of Public Works
dpw.lacounty.gov
(626) 458-4319
wjohnson@dpw.lacounty.gov

## Slide 15
Bullpen Slides

## Slide 16
Receiving Water/LCC Metals TMDL Monitoring Site
LACFCD and County to partner with Los Cerritos Channel Group for Receiving Water/LCC Metals TMDL site.
Existing City of Long Beach Mass Emission Site at Stearns Street.
Site has been operational since 2000.

## Slide 17
Storm Water Outfall/LCC Metals TMDL
Group to partner with LCC Group for a new site SB10
TMDL site along Palo Verde Drain.
Adjacent to invert access ramp.
An autosampler to be installed.
Lakewood
Long Beach
SB10

## Slide 18
Receiving Water TMDL Site: Dominguez Channel and Greater Los Angeles/Long Beach Harbors Toxics TMDL
County and LACFCD are both partners with the Greater Harbors Regional Monitoring Coalition

## Slide 19
Receiving Water TMDL Site: Colorado Lagoon Toxics TMDL
LACFCD partnering with City of Long Beach on Colorado Lagoon Toxics TMDL plan preparation and monitoring.
WS1 -4: Water Quality Sites
F1-2: Fish Sampling Sites
M1-3: Mussel Collection Sites