## Slide 1: Recommendations for Determining Regional Instream Flow Criteria for Priority Tributaries to the Sacramento-San Joaquin Delta A Report to the California State Water Resources Control Board
Committee Members
Cliff Dahm - University of New Mexico
Kirk Winemiller – Texas A&M University
Marty Kelly – Southwest Florida Water Management District (retired)
Sarah Yarnell – University of California-Davis
March 19, 2014
Notes: 1

## Slide 2: Rivers and Flows – Scientific Foundation
Global crisis in freshwater biodiversity – 0.8% of the Earth’s surface is freshwater with 6% of the described species (~100,000) on Earth found in freshwaters with the highest percentage of threatened, endangered, or recently extinct species (~40%)
Diminished flows are the primary predictors of biological integrity for fish and aquatic invertebrates in the US relative to eight chemical and physical properties
The flow regime is more than just volumes of water; magnitude, frequency, duration, timing, and rate of change of flows all need consideration

## Slide 3: Committee Charge
Identification of methodology that is scientifically defensible, cost-effective, representative at the watershed scale and timely relative to implementation
Input on how recommended methodology or methodologies can be augmented or refined in the future
How to develop flow criteria that apply to the majority of the watershed within a tributary that addresses multiple species, different life stages, and different fluvial processes

## Slide 4: Panel Recommendation – Use of a Hybrid Approach
stream and river classification based on geomorphic, hydrologic, geographic, and/or faunal characteristics
hydrologic analyses that separate the hydrograph into flow regimes (blocks) and examine historical changes
assessment of whether any site-specific field work is required in the catchment or river reach to address specific information gaps
extrapolation of understanding of flow-ecology relationships from other sites to the study catchment or segment
production of an environmental flow regime that meets the needs of species and ecosystem processes in the system
assuring clear and transparent dialogue and interaction between scientists and stakeholders
designing an effective adaptive management protocol with robust implementation measurements to support the decision-making process

## Slide 5
“The minimum flow for a given watercourse shall be the limit at which further withdrawals would be significantly harmful to the water resources or ecology of the area.” Section 373.042 Florida Statutes
Environmental flow is the term for the amount of water needed in a
watercourse to maintain healthy, natural, ecosystems. Only a few
countries, such as Australia, South Africa, and the United Kingdom
have integrated the concept into water management.
Setting Flow Criteria for Estuaries and Rivers
in the Southwest Florida Water Management District (SWFWMD)

## Slide 6
Building Block Approach – Florida Example

## Slide 7: Habitat Suitability Curves
Key Non-native Fish Species
Key Native Fish Species
Key Aquatic Macroinvertebrates
Dominant Riparian Plants
Riparian Dependent Bird Species

## Slide 8: Setting Estuarine Flow Criteria in Texas (River Flow Criteria Already Adopted)
“basin and bay expert science team shall develop environmental flow analyses and a recommended environmental flow regime for the river and bay system … through a collaborative process designed to achieve consensus”
“must consider all reasonably available science, without regard to the need for the water for other uses, and … the recommendations must be based solely on the best science available”
Texas Water Code §11.02362 (m)
Senate Bill 3 - 2007
Notes: 8

## Slide 9: Setting Estuarine Flow Criteria in Texas (continued)
Statewide Environmental Flows Science Advisory Committee
Bay/Basin Expert Science Teams
Address Seasonal and Yearly Fluctuations
Support a “Sound Ecological Environment”
Maintain Productivity, Extent, and Persistence of Key Habitats in the Seven Major Estuaries
Stakeholder Committee and State Agencies
Notes: 9

## Slide 10: Setting Flow Requirements – Examples from California
Restoration of the spring snowmelt recession pattern
Restoration of a more natural flow regime on Putah Creek
Adaptive management and reconciliation on the North Fork Feather River

## Slide 11: Some General Principles For Sustaining Healthy Rivers
A modified flow regime should mimic the natural one, so that the natural timing of different kinds of flows is preserved
Most water should be harvested from a river during wet months; little should be taken during dry months
The seasonal pattern of higher baseflows in wet seasons should be retained
Floods should be present during the natural wet season
The duration of floods could be shortened
It is better to retain certain floods at full magnitude and to eliminate others entirely than to preserve all or most floods at diminished levels
The first flood (or one of the first) of the wet season should be fully retained