## Slide 1
Lake Tahoe: Journey to
Lake Clarity Crediting Program
California Regional Water Quality Control Board
Lahontan Region
Dr. Amy Horne
Lahontan Water Board Member
Robert Larsen
Environmental Scientist
18 May 2017

## Slide 2: What is the Lake Tahoe TMDL?
A science-based plan to restore
Lake Tahoe’s clarity

## Slide 3: Lake Tahoe TMDL Phases
Science Phase (1959 – 2010)
  What pollutants are causing clarity loss?
  How much of each pollutant reaches the lake?
  How much of each pollutant can the lake receive and still meet clarity goal?
Regulatory Strategy Phase (2005 – 2010)
  What strategy should we use to reduce pollutant loading?
  How do we regulate pollutant load reduction?
Implementation Phase (2010 – 2075?)
  Are we achieving expected reductions in pollutant loading?
  Is lake clarity improving?

## Slide 4: Science Phase: 1959 - 2010
1959: Dr. Charles Goldman began monitoring lake clarity
Initial hypothesis: N, P causing clarity loss
1968: All wastewater exported from Tahoe Basin
Remaining N, P from non-point sources
2005: Scientists find new culprit: fine sediment particles (FSP)

## Slide 5: What are the Sources of Nitrogen?
Chart: Total Nitrogen Estimates: Percent Contribution per Source Category
| Urban Upland | Non-urban Upland | Stream Channel Erosion | Atmospheric Deposition | Groundwater | Shoreline Erosion
 | 0.15869 | 0.15617 | 0.0050378 | 0.54912 | 0.12594 | 0.0050378

## Slide 6: … and Phosphorus?
Chart: Total Phosphorus Estimates: Percent Contribution per Source Category
| Urban Upland | Non-urban Upland | Stream Channel Erosion | Atmospheric Deposition | Groundwater | Shoreline Erosion
 | 0.38298 | 0.25532 | 0.021277 | 0.14894 | 0.14894 | 0.042553

## Slide 7: … and Fine Sediment Particles?
(particles less than 16 micrometers)

## Slide 8: TMDL Science Conclusions
Two- thirds of clarity loss caused by FSP (<16 micrometers)
Total FSP Load = 481 x 1016 Particles
Need to reduce FSP load by 32% to reverse clarity loss
Urban accounts for 72% of FSP

## Slide 9: Regulatory Strategy Phase 2005 - 2010
For each source category, experts quantified different options to reduce N, P, FSP loads
TMDL implementation strategy based on cost-effectiveness and feasibility

## Slide 10
Urban Atmospheric Forest Streams
Current Particle Load and Percent Reduction Target
31%
34%
12%
53%
FSP Load Reduction Targets

## Slide 11: Urban FSP Reduction Timeline
Chart: 
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65
 | 10 | 19 | 32 | 35 | 38 | 42 | 44 | 47 | 51 | 55 | 58 | 61 | 65
Time in Years
% FSP Load Reduction
2016 target
2021 target

## Slide 12: Municipal NPDES Storm Water Permit
Performance based regulation
Requires municipalities to reduce FSP as percent of 2004 baseline
Loading time step is average annual
Actions to reduce FSP also reduce N, P

## Slide 13: Storm Water Permittees
Placer County
El Dorado County
City of South Lake Tahoe
(CalTrans: Tahoe-specific requirements)

## Slide 14: Implementation Phase 2010 – 2075?
Challenges:
Link action to expected benefits
Track progress at municipal and annual scales
Encourage jurisdictions to cooperate

## Slide 15: Lake Clarity Credit
Standard Metric
One Lake Clarity Credit = 1 x 1016 FSP

## Slide 16: Lake Clarity Credit Targets Minimum Number of Credits
Jurisdiction | 2016 | 2021
El Dorado | 220 √ | 342
Placer | 260 √ | 554
South Lake Tahoe | 190 √ | 521

## Slide 17: The Lake Clarity Crediting Program Process

## Slide 18: Many Ways to Earn Credits

## Slide 19: Municipality Prioritizes Actions to Earn Credits
Emphasis on surface water connectivity
Modelling tools facilitate meaningful alternatives analysis
Credit award requires demonstrated maintenance

## Slide 20
Storm Water Treatment
Reduce Pollutant Potential
(Source Control)
Urban Catchment
Maintain BMPs
Lake Clarity Crediting Program & Implementation Tools
Private BMPs & Muni Ordinances
Sand & Sweep
Road Operations
Inspect & Enforce
WQ Improvement Projects
Pollutant
Load
Reduction
Model
Rapid
Assessment Methods
Accounting and Tracking Software
Notes: 20

## Slide 21: Lake Clarity Crediting Program

## Slide 22: Sharing Credits Across Jurisdictions
City/CalTrans/Private Property and $$
Capital Cost >$15M
Community facilities district funds maintenance

## Slide 23: LCCP Report Card
Water Board:
  Focuses municipalities on effective actions
  Creates incentives for innovation
  Links project-level actions to Lake Tahoe TMDL
Municipalities:
  Program flexibility
  Regulatory predictability
  Opportunities to cooperate

## Slide 24: LCCP Report Card
Funding Agencies:
  Guidance for awarding grants
  Evaluate project effectiveness
Stakeholders:
  Most accept regulatory strategy
  Some distrust models
  Equity concern

## Slide 25: LCCP Report Card
Lessons Learned:
Develop tools concurrent with policy
Provide consistency and predictability
Share risks associated with uncertainty
Continually update tools and software to incorporate new science
Regularly engage with partners to adaptively manage the program

## Slide 26: Is Lake Clarity Improving?

## Slide 27: Questions?