## Slide 1: Update on the Industrial Storm Water Program and Implementation of the Renewed General Permit
Mona Dougherty, P.E.
North Coast Regional Water Quality Control Board
Item No. 7
May 18, 2017
Santa Rosa, California

## Slide 2: Presentation Outline
Industrial storm water program overview
Significant changes in the renewed permit
Review of the 2015-2016 annual reports
Example of BMPs at North Coast facilities
  Successes and challenges
Current and future priorities

## Slide 3: Storm Water Program
Point source national pollutant discharge elimination system - NPDES
Industrial, construction, and municipal
North Coast Region
  Industrial: Paul Keiran
  Municipal: Colleen Hunt
  Construction: Devon Jorgenson
  Scientific Aide: Shawn Agarwal
  Program manager: Mona Dougherty

## Slide 4: Industrial Storm Water Overview
Make, move, mine products
Program based on best management practices (BMPs)
  No numeric effluent limits
  BMPs should be as simple and as low maintenance as is effective
Pollutants: sediment, metals, hydrocarbons, pollutants that effect pH

## Slide 5
North Coast Industrial Facilities
Created by Shawn Agarwal
May 12, 2017

## Slide 7: Industrial Storm Water Overview
Types of facilities not included:
  Kennels, boarding, and veterinarians
  Nurseries, landscaping stores, farm supply stores, home improvement stores, winery pomace and agriculture composting operations
  Auto repair, auto dealerships
  Industries on tribal lands – USEPA permit

## Slide 8: Industrial Storm Water General Permit (IGP) Overview
1987 - Clean Water Act amended to include industrial and municipal storm water
1991 and 1997 – Previous versions of IGP adopted
2014 - Reissued IGP adopted
July 1, 2015 - Reissued IGP became effective

## Slide 9: Industrial Storm Water General Permit (IGP) Overview
IGP adopted by State Water Board
IGP requires monitoring and annual reporting
Pollutants compared to benchmark levels from USEPA’s 2008 Multi-Sector General Permit for storm water discharges
Best available technology economically achievable (BAT)/best conventional pollutant control technology (BCT)

## Slide 10: Reissued Industrial Storm Water General Permit and Significant Changes from the Previous Permit

## Slide 11: Significant Changes
No Exposure Certification (NEC)
Notice of non-applicability (NONA)
Additional sampling: four qualifying storm events, all discharge points
Visual monitoring: all discharge points, industrial activities and storage areas

## Slide 12: Significant Changes
U.S.EPA Benchmark Levels are now Numeric Action Levels (NALs)
Exceedances require:
  Exceedance Response Action Report
  Additional BMPs to avoid future exceedances
  Qualified Industrial Storm Water Practitioner (QISP)

## Slide 13: Significant Changes
Three levels of regulation
  Baseline: Permittees start here
  Level 1, exceedance of NAL(s): ERA report, additional BMPs, QISP
  Level 2, exceedance of NAL(s) next year: More robust report, additional BMPs

## Slide 14: Significant Changes
Electronic reporting required: statewide database (SMARTS)
Clean Water Act 303(d) List evaluation
Design standards for treatment control BMPs
Requirements for discharges to Areas of Special Biological Significance

## Slide 15: Review of 2015-2016 Reporting Year
  First annual report submitted under the new IGP

## Slide 16: Review of 2015-2016 Reporting Year
  Approximately 450 active facilities in North Coast Region
  84 facilities have received NEC
  7 facilities have received NONA

## Slide 18: Review of 2015-2016 Reporting Year
  98 facilities submitted an annual report, did not sample
  Burden to prove discharge lies with Regional Board staff
  Statewide issue – benefits of non-compliance
  Prevents us from assessing permit compliance and potential threats to water quality

## Slide 19: Review of 2015-2016 Reporting Year
  65 facilities were moved from baseline to level 1
    Most common exceedances: total suspended solids (TSS), iron, and aluminum
    Exceedance response action (ERA) reports were due January 1, 2017
    64 facilities have submitted the ERA report

## Slide 21: Industrial Storm Water General Permit Implementation Improved BMPs at North Coast Industrial Facilities

## Slide 22
Packed gravel lumber storage yard at sawmill

## Slide 23
Resulting turbid storm water discharge

## Slide 24
Paved the following year

## Slide 25
North Coast sawmill – Chemical Oxygen Demand

## Slide 26
Same channel two years later

## Slide 27
Boat repainting facility with direct discharge to Humboldt Bay

## Slide 28
Dissolved and total metals discharged directly to bay

## Slide 29
Advanced multi-stage treatment system

## Slide 30
Exposed pile at recycling center – Biochemical Oxygen Demand (BOD), Total Suspended Solids (TSS)

## Slide 31
Canopy cover constructed

## Slide 32
Sand, paper, carbon filtration system

## Slide 33
Auto wrecking yard

## Slide 34
Hydrocarbons and heavy metals

## Slide 35
25,000 gallon holding tank and multi-stage treatment

## Slide 36
Large composting operation

## Slide 37
Discharged leachate causing potential surface and ground water impacts

## Slide 38
Berm and collection system surrounding composting operations

## Slide 39
Leachate/storm water collection pond

## Slide 40: Challenging Issues

## Slide 41
Nutrients and TSS from compost and soil mixing operations

## Slide 42
Tannin and lignin from sawdust and wood chip piles and sediment (sawmills, cogeneration plants, soil mixers)

## Slide 43
TSS (construction debris yards, trucking company gravel lots)

## Slide 44
Putrescible waste from uncovered recycling operations – BOD, Nutrients

## Slide 45: Compliance Challenges
Dirt! Most NAL exceedances occur from sediment discharges
Lack of or inadequate structural BMPs
  Roofing, paved work areas, adequate pond size
Off-site run on
Decreasing number of permittees sampling

## Slide 46: Prioritization of Inspections
Facilities that did not sample
Facilities that have an exceedance multiple years in a row
New enrollees
Facilities with NEC or NONA
Non-filers

## Slide 47: Current Priorities
  Enforcement
    Failure to submit reports
    Failure to sample
    Inadequate BMPs
    Non-filers
    Enroll soil mixers in IGP

## Slide 48: Future Priorities
  Enroll mobile industries
  Work with sites not subject to storm water program with water quality issues

## Slide 49: Thank you!
Questions?