GRANT SUMMARY

Completed Grant Summaries are made available to the public on the State Water Resources Control Board’s (SWRCB) website at http://www.waterboards.ca.gov/nps/formsandsummaries.html.

# Use the tab and arrow keys to move through the form.  If field is not applicable, please put N/A in field.

Date filled out:  10/10/05

| Grant Information: Please use complete phrases/sentences. Fields will expand as you type. |
| --- |
| 1. Grant Agreement Number: 04-197-556-0 |
| 2. Project Title: Merrill Davies Restoration |
| 3. Project Purpose – Problem Being Addressed: On Davies Creek, an old railroad was constructed in the channel and on the floodplain and has redirected and confined the flows of the creek. The railroad construction caused riparian habitat to be lost or degraded, caused the stream to downcut in several places, and has created a headcut that eroded up into the lower end of Sardine Meadow, lowering the water table causing the meadow habitat to degrade. The existing road at the bridge site has constricted the flood plain of theCreek. Likewise on Merrill Creek, another railroad grade was constructed across the floodplain and has confined the flows of the creek. The existing road has constricted the flood plain of theCreek at the bridge site. |
| 4. Project Goals |
| a. Short-term Goals: Short term goals are 1) restoring the confluence of Davies and Merril creeks, and 2) restoring a portion of the Merril Creek floodplain. |
| b. Long-term Goals: Long term goals are to reduce active erosion within the watersheds, reduce the potential for future erosion, improve the quality of surface runoff by improving surface filtration, restore floodplain functions, increase flood attenuation potential, increase ground water storage, and improve and increase the riparian habitat in the area. |
| 5. Project Location: (lat/longs, watershed, etc.) 10S 4376453mN, 749883mE |
| a. Physical Size of Project: (miles, acres, sq. ft., etc.) 13.2 acres; 7,900' pond and plug; 7,000'upland grade removal; 3,000' upland road removal; 100' diversion berm removal |
| b. Counties Included in the Project: Sierra County |
| c. Legislative Districts: (Assembly and Senate) 01 Senate; 03 & 04 Assembly |
| 6. Which SWRCB program is funding this grant? Please “X” box that applies. |
|  | Prop 13 | Prop 40 | Prop 50 | EPA 319(h) | Other |
| Grant Contact: Refers to Grant Project Director. |
| Name: Lisa Wallace | Job Title: Executive Director |
| Organization: Truckee River Watershed Council | Webpage Address: www.truckeeriverwc.org |
| Address: PO Box 8568, Truckee, CA 96162 |
| Phone: 530-550-8760 | Fax: 530-550-8761 |
| E-mail: lwallace@truckeeriverwc.org |
| Grant Time Frame: Refers to the implementation period of the grant. |
| From: February 1, 2005 | To: January 31, 2007 |
| Project Partner Information: Name all agencies/groups involved with project. USFS Tahoe National Forest |
| Nutrient and Sediment Load Reduction Projection: (If applicable) |

Please provide a hard copy to your Grant Manager and an electronic copy to your Program Analyst for SWRCB website posting.  All applicable fields are mandatory.  Incomplete forms will be returned.