## Slide 1: PART 2 DOWNSTREAM TEMPERATURE BENEFIT
Conducted by Tom Payne and Associates

## Slide 2
Canyon Dam Release
Prattville Intake

## Slide 3: Stream Network Temperature Model (SNTEMP)
Public domain developed by USFWS
A complete full suite heat flux model
Stream geometry, riparian and topographic shading
Tributaries and accretion flows
Meteorological correction for elevation change
Temporal and spatial water temperatures
UNFFR - daily average temperatures with distance

## Slide 4: Temperature Profiles with Distance
Canyon Dam

## Slide 5: Temporal Temperature Distribution

## Slide 6: SNTEMP Modeling Accuracy
2000
2001
Correlation
Mean
Probable
Correlation
Mean
Probable
Station
Coefficient
Error
Error
Coefficient
Error
Error
(R2)
(0C)
(+/-0C)
(R2)
(0C)
(+/-0C)
Seneca Reach Stream Station
At Seneca Bridge (NF3)
0.9412
-0.08
0.22
0.95.71
-0.06
0.21
Upstream Caribou Powerhouse (NF4)
0.9485
0.03
0.27
0.9695
0.27
0.18
Lower Butt Creek Reach Stream Station
At mouth (BC3)
0.9295
-0.05
0.12
0.9431
0.02
0.11
Belden Reach Stream Station
Upstream of Queen Lily (NF6)
0.9962
0.14
0.10
0.9928
0.03
0.15
Gansner Bar Campground (NF7)
0.9883
0.09
0.18
0.9849
0.04
0.23
Upstream Belden Powerhouse (NF8)
0.9973
0.00
0.11
0.9917
-0.01
0.19

## Slide 7: Modeling Conditions (SNTEMP)
Steady State
Starting Conditions (SC) from MITEMP predictions
Bracket temperature range by 3 probabilities of occurrence (50%, 25% and 10% exceedance levels)
  50%  Normal Case (50% SC/Normal met/Normal WY accretion)
  25%  Reasonable Extreme (25% SC/Warm met/Dry WY accretion)
  10%  Rare Events (10% SC/Warm met/ Dry WY accretion)
Four instream flow schedules (associated with Wet, Normal, Dry and Critical Dry water year types) Instream Flow Schedule
Four months in the summer (June-September)
3 X 4 X 4 = 48

## Slide 8: Modeled Operation Scenarios
Baseline – Existing Prattville/Existing Butt Valley Reservoir (BVR)
Modified Prattville Intake*/Existing BVR *=curtain no. 4 in IIHR study
Same as Scenario 2 with Levees removed/Existing BVR
Same as Scenario 3 with blending of Canyon Dam releases/Existing BVR

## Slide 9
NFFR above Caribou

## Slide 10: Seneca Reach NFFR above Caribou

## Slide 11: Daily Average Temperature – Normal Case – NFFR above Caribou

## Slide 12: Seneca Reach NFFR above Caribou

## Slide 13: Daily Average Temperature – Reasonable Extreme – NFFR above Caribou

## Slide 14: Seneca Reach NFFR above Caribou

## Slide 15: Daily Average Temperature – Rare Events – NFFR above Caribou

## Slide 16
NFFR above Caribou
NFFR above East Branch
NFFR above Belden PH

## Slide 17: Belden Reach NFFR above East Branch

## Slide 18: Daily Average Temperature – Normal Case – NFFR above East Branch

## Slide 19: Daily Average Temperature – Reasonable Extreme – NFFR above EB

## Slide 20: Daily Average Temperature – Rare Events – NFFR above EB

## Slide 21: Belden Reach NFFR above Belden PH

## Slide 22: Daily Average Temperature – Normal Case – NFFR above Belden PH

## Slide 23: Daily Average Temperature – Reasonable Extreme – NFFR above Belden PH

## Slide 24: Daily Average Temperature – Rare Events – NFFR above Belden PH

## Slide 25: Instream Flow Schedule
Seneca Reach Instream Flow Release at Canyon Dam (CFS)
Water Year Type June July August September
Critical Dry 80 75 60 60
Dry 110 80 70 60
Normal 125 90 80 60
Wet 150 95 80 60
Belden Reach Instream Flow Release at Belden Dam (CFS)
Water Year Type June July August September
Critical Dry 90 80 75 75
Dry 160 130 110 100
Normal 225 175 140 140
Wet 225 175 140 140 Modeling Conditions (SNTEMP)