## Slide 1: Truckee River Watershed Council Truckee River Sediment TMDL
Lahontan Regional Water Quality Control Board
Beth Christman & Lisa Wallace
June 19, 2014

## Slide 2: Presentation Outline
Truckee River TMDL Background
TRWC Monitoring Program
Key Results
Discussion of Findings

## Slide 3: Middle Truckee River Sediment TMDL
Truckee River listed for excess sediment
Included on 303(d) list in 1991 based on biological impacts – best professional judgment
TMDL adopted in 2008

## Slide 4: TMDL Standards
Watershed-wide TMDL
Numeric target: 25 mg/L suspended sediment concentration (SSC)
Implementation targets
  Road sand tracking and recovery
  Ski area BMPs
  Dirt road maintenance/decommission
  Legacy site restoration/BMP installation

## Slide 5: Where are we now?
TRWC began TMDL monitoring in 2010
  Only TMDL-specific monitoring
We now have data that shows biological impairment
Current TMDL standard not suited to assess biological impact
Preliminary meeting with LRWQCB staff

## Slide 6: Why TRWC is Monitoring
Lack of strong monitoring plan in the adopted TMDL
Need for watershed-based vs. individual permittee reports
Inconclusive biological studies – need for more data
Establish “baseline” conditions to track progress

## Slide 7: Monitoring Plan Elements
Macroinvertebrates
  Index of Biological Integrity study - reference test
  Patch-scale sediment
  Repeat LRWQCB 2004 sampling below tributaries
  Studies completed 2011
Sediment and Turbidity
  Near continuous turbidity
  Suspended sediment grab samples
  Bed surveys
  Funded through WY2014

## Slide 8: Partners
Town of Truckee
Placer County

## Slide 9: Technical Advisory Committee
CA Department of Water Resources
Lahontan Regional Water Quality Control Board
Placer County
Town of Truckee
U.S. Geologic Survey

## Slide 10: Elements Presented Today
Macroinvertebrate – reference/test
Macroinvertebrate – patch-scale
  Studies by UCSB- SNARL, Dr. David Herbst
Suspended sediment and turbidity summary
  Studies by Balance Hydrologics

## Slide 11: Key Points
1. Biological data shows impairment
2. Disconnect between current numeric standard and detecting impairment

## Slide 12: Bioassessment
Reference/Test Study (2010)
Patch Scale Fine Sediment Study (2011)

## Slide 13: Bioassessment 101
Using biological organisms to assess water quality
Direct indicator of stream environment
Benthic macroinvertebrates most common
Different types of insects tolerate poor water quality – assigned a “tolerance value”

## Slide 14: Bioassessment “Jargon”
Index of Biological Integrity (IBI) common analysis tool
  Developed specific to a region
  Allows to look at just one “score”
EPT = Ephemeroptera (mayflies), Plecoptera (stoneflies), and Trichoptera (caddisflies)
Tolerance Value: 0-10 assigned to each species
BMI = Benthic macroinvertebrate

## Slide 15: Reference/Test Results – IBI Scores
Middle Truckee samples all scored as impaired (red) or partially supporting (yellow)
Reference sites scored as partially supporting or supporting (green)

## Slide 16: Patch Scale Analysis
Tightens up relationship between sediment and biota
Collect BMIs from small patches over a range of fine sediment cover (0-100%)
Survey reaches of Middle Truckee to understand pattern of fine sediment deposition

## Slide 17
BMI Monitoring Locations – Patch Scale Study

## Slide 18: BMI Density Declines with Increased Fines
0% 1-20% 21-40% 41-60% 61-80% 81-100%
Percent Cover by Fines and Sand
# orgs/m2

## Slide 19: %EPT Decreases with Increased Fines
0% 1-20% 21-40% 41-60% 61-80% 81-100%
Percent Cover by Fines and Sand
%EPT

## Slide 20: % Midges Increases with Increased Fines
0% 1-20% 21-40% 41-60% 61-80% 81-100%
Percent Cover by Fines and Sand
% Chironomidae

## Slide 21: Fewer Intolerant, More Tolerant Species with Increased Fines
0% 1-20% 21-40% 41-60% 61-80% 81-100%
Percent Cover by Fines and Sand

## Slide 22: Summary of Biological Impacts
Food quality and quantity decreases
  Fewer insects
  Smaller body size
Sensitive taxa are lost from the community
Sediment thresholds
  Impacts appear >20% fine and sand cover
  Impacts significant at 80%

## Slide 23: How Prevalent is Sediment Deposition?

## Slide 24: Suspended Sediment Results
Disconnect between bioassessment and sediment data

## Slide 25: Sediment and Turbidity Monitoring Stations on 3 key tributaries

## Slide 26: Suspended Sediment/Turbidity Results
Data from WY 2010 – 2013
Tributaries are meeting suspended sediment concentration standard of 25 mg/L 90% of the time

## Slide 27: Beneficial Uses are Impaired
Biological data show increased sediment = decreased condition
Sediment deposition is fairly widespread in sampling reaches
SSC data suggest current standard is largely met in 3 monitored tributaries

## Slide 28: Next Steps
Additional standard for Truckee River that directly assesses impacts to beneficial uses
  Biological?
  Deposited Sediment?
Fund additional monitoring
  Sediment distribution
  Additional bioassessment sites
  Depending on standard:
    Annual cost $30,000 - $150,000+
    Study period 3-5 years

## Slide 29: Questions?
Reports available at: www.truckeeriverwc.org
Beth Christman
(530) 550-8760
bchristman@truckeeriverwc.org

## Slide 30: Additional Information – Suspended Sediment

## Slide 31: Total Loading from Tributaries

## Slide 32: Relationship to TMDL SSC Standard?
Water Year 2012 Data – Trout Creek

## Slide 33: Relationship to TMDL SSC Standard?
Water Year 2012 Data – Donner Creek

## Slide 34: Relationship to TMDL SSC Standard?
Water Year 2013 Data – Cold Creek

## Slide 35: Key Sediment/Turbidity Conclusions
Tributaries are meeting suspended sediment concentration standard of 25 mg/L 90% of the time
Lower Donner watershed extremely high load contribution
Early season rain storms result in significant loading

## Slide 36: Farad Data
From LRWQCB, 2011. Truckee River Status Report