## Slide 1
Water Quality Monitoring and Water Management
4 April 2001
Water Resources Management in the Santa Margarita River

## Slide 2: Today’s Presentation
Santa Margarita River Challenges
Addressing the Challenges
Framework Monitoring Plan Overview
Future Needs in the Watershed

## Slide 4: The Challenges

## Slide 5: There are water resources challenges to agencies & individuals in the watershed
Listed reaches do not meet water quality standards (CWA 303(d) Listing)
Required Total Maximum Daily Load process will allocate loads or load reductions among sources
Assimilative capacity of the system is an issue to all dischargers
Habitat health especially for listed species
Water rights and water management have water quality linkages
Ongoing & anticipated growth in the watershed has relationship to all the above

## Slide 6
1998 CA 303(d) Listed Sites in Santa Margarita Watershed

## Slide 7: Total Maximum Daily Load
Sum of individual wasteload allocations for point sources, load allocations for non-point sources, and natural background pollutants, plus a margin of safety.
Can be expressed in terms of mass loads or other appropriate measures.
TMDLs are usually based on readily available information and studies.
Santa Margarita Lagoon TMDL has potential to impact all upstream point sources and non-point sources.

## Slide 8: Beneficial Uses
Beneficial use designations could significantly impact organizations in the watershed
  GWR: Groundwater recharge
  REC-1: Contact water recreation
  COLD: Cold freshwater habitat
  RARE: Rare, threatened or endangered species
Are the beneficial use designations justified & documented by monitoring?
Monitoring required for an accurate designation

## Slide 9: Will a “Cold” designation ultimately require temperature control activities in the river?

## Slide 10: Agency floats plan to protect trout habitat March 12, 2001The Orange County Register
…. urge the National Marine Fisheries Service to declare a creek near San Clemente a protected habitat for steelhead…. The creek … meanders 8 miles from the Cleveland National Forest through Camp Pendleton to the beach at Trestles.
…. Until 1999, federal regulators thought Southern California steelhead no longer existed south of Malibu Creek…. Now environmental groups are pushing to extend federal protections south from Malibu Creek to San Mateo Creek.
…. "Our goal," he said, "is to restore the habitat within the stream back to what it was in the 1940s."
Just north of the Santa Margarita River:

## Slide 11: Existing and Future Land Use
Tremendous growth in Temecula, Murrieta, and along the Interstate 15-215 corridor in the last ten years. Continued growth is anticipated for the foreseeable future
The portion of San Diego County in the Watershed along the Interstate 15 corridor also continues to grow
Preliminary review compares “Current” to “Future”
  Change in use
  Change in percent urbanization of subwatershed
Focus sampling to anticipate & measure changes

## Slide 12: Preliminary review illustrates anticipated urbanization in the watershed

## Slide 13: Point Source Discharges
Camp Pendleton:
  5 NPDES permits associated with Wastewater Treatment Plants.
  Total discharge of 6.6 mgd
RCWD:
  NPDES permit for discharge of 2.0 mgd of tertiary treated wastewater into Murrieta Creek.

## Slide 14: Non-Point Source Discharges
Non-point source discharges are reported to be the largest contributor to surface water pollution in the watershed.
Non-point source discharges are typically associated with urban or agricultural runoff
Factors that affect non-point source discharges
  Existing and future land use
  Stormwater Best Management Practices
  Phase II stormwater regulations in 2003.

## Slide 15: Preliminary List of Species to be Addressed in the Watershed
Animal Species
CA red-legged frog
Arroyo toad
Arroyo chub
Tidewater goby
Southwestern Pond Turtle
Least Bells Vireo
Plant Species
San Diego ambrosia
Nevin’s Barberry
Thread-leaved Brodiaea
Salt marsh bird’s-beak
Slender-horned spineflower
Coulter’s goldfields
Parish’s meadow-foam

## Slide 18: Addressing the Santa Margarita River Challenges

## Slide 19: Addressing the Challenges
Good data is needed to make good decisions
  Was adequate data available for Basin Plan & 303(d) listing?
  Is adequate data available to set TMDL allocations?
A number of organizations are independently collecting data – a coordinated effort is needed to address the significant challenges
USBR has funded a Framework Plan for integrated monitoring in the Watershed

## Slide 20: The Framework Monitoring Plan Guidance
Santa Margarita River Watershed Water Quality Monitoring Group working with the USBR
  Representatives from 29 organizations
  List of members expanded over the course of the planning effort
SMR Group developed list of goals for monitoring:
  facilitate development of water resources to meet demands in a manner consistent with sustainable use, human safety, and habitat and ecological needs, including protection of listed species

## Slide 21: Membership List of Santa Margarita River Watershed Water Quality Monitoring Group (SMR Group)

## Slide 22
CALTRANS
Cahuilla Band of Mission Indians
CA Department of Water Resources
Conservation Biology Institute
Eastern Municipal Water District
EMA Resource Conservation District
Fallbrook Public Utilities District
Fallbrook Naval Weapons Station
Hines Nursery
Marine Corps Base, Camp Pendleton
Metropolitan Water District of Southern California
Mission Resource Conservation District
Murrieta County Water District
Pauma-Yuima Band of Mission Indians
Pechanga Band of Mission Indians
Ramona Band of Mission Indians
Rancho California Water District
Riverside County FC&WCD
San Diego County
San Diego County Water Authority
San Diego RWQCB
San Diego State University
Santa Margarita Watermaster
U.S. Bureau of Indian Affairs
The Nature Conservancy
U.C. Cooperative Extension
U.S. Bureau of Reclamation
U.S. Environmental Protection Agency
U.S. Geological Survey

## Slide 24: Goals of the FMP - as identified by the SMR Group

## Slide 25
Assessment of regarding achievement of existing water quality standards
Support scientific development of TMDLs
Assess assimilative capacity for nutrients and total dissolved solids (TDS);
Determine relationships between habitat health and water quality
Identify water quality issues related to water supply alternatives
Develop a scientific basis for decisions regarding CWA §303(d) listing;
Identify the causes of beneficial use impairments by contaminant and source,
Quantify pollutant loading from point and non-point source discharges, including stormwater;
Evaluate sediment transport;
Evaluate effectiveness of stormwater best management practices (BMPs);
Verify regulatory compliance (as a replacement of all existing permit requirements for monitoring) and support for future permitting;
Facilitate water recycling in the watershed.

## Slide 26: Framework Monitoring Plan Overview

## Slide 27: Framework Monitoring Plan
Statement of objectives:
  …Monitoring plan to meet local goals and impending regulatory mandates
Project description:
  …framework-monitoring plan with recommendations for fully developing the plan.
Duration of Planning Effort
  November 2000 to April 4, 2001

## Slide 28: Framework Plan Products
Basemap highlighting
  Current & proposed sampling locations
  Drivers for change (e.g., 303d, hydrology,land use)
Table of locations & parameters
Narrative
PowerPoint Presentation

## Slide 29: Overlay Analysis of Data Used to Site Preliminary Sampling Locations
Hydrologic units
Stream gage locations
Point discharges
Current sampling locations
T & E species locations
303d list
  Hydro Unit
  Pollutant/Stressor
Land use
  Current
  Locations of change
Agency boundaries

## Slide 30: Proposed Monitoring Locations

## Slide 31: Monitoring Locations on Santa Margarita River

## Slide 32: Monitoring Locations on Santa Margarita River
NPDES & TMDL
Base Program & NPDES
TMDL
Habitat Issues
TMDL
NPDES & TMDL

## Slide 33: Monitoring Locations on Murrieta Creek

## Slide 34: Monitoring Locations on Murrieta Creek
TMDL
TMDL & Assimilative Capacity
NPDES & TMDL
NPDES, TMDL, and Sediment

## Slide 35: Anticipated Future Urban Land Uses Drive Monitoring Locations

## Slide 36: Monitoring Locations on Temecula Creek
TMDL
TMDL and Habitat

## Slide 37: Projected Urban Growth by SANDAG Drives Monitoring

## Slide 38: Future Needs in The Watershed

## Slide 39: Future Activities to Address Challenges
Complete a Comprehensive Plan through partnership of USBR & SMR Group members
  Support Congressional funding
  Provide local contribution
Future tasks are needed
  Evaluate the data
  Set stage for rationale TMDL process
  Link water quality to water supply and management

## Slide 40: A Comprehensive Monitoring Plan is the Next Step to Address the Challenges
Create of database design for all water quality sampling;
Prepare a standard GIS format for the SMR Watershed;
Analyze water quality data;
Develop a screening level model to identify key water quality areas:
Develop a Stormwater BMP Pilot Program;
Prepare standard Sampling and Analysis Plan
Coordinate with SDRWQCB for approval

## Slide 41: Pilot Testing BMPs
Quantify water quality benefits,
Assess technical feasibility,
Estimate Costs, and
Operation and maintenance requirements
Opportunities and constraints relative to
  siting,
  design,
  construction

## Slide 42: Other Tasks to Address Goals Using Monitoring Program
Support scientific development of TMDL;
Estimate assimilative capacity of the SMR;
Identify relationship between habitat health & water quality;
Identify relationship between water supply rights & water quality;
Address water recycling water quality issues;
Identify beneficial use impairments;
Support regulatory compliance using integrated data;
Support implementing Phase II stormwater regulations
Apply new data to existing sediment transport model