## Slide 1: SOUTHERN DELTA ELECTRICAL CONDUCTIVITY WATER QUALITY OBJECTIVES
PRESENTATION BY
WILLIAM R. JOHNSTON

## Slide 2: SWRCB based the Southern Delta Agricultural Water Quality Objectives on:
Calculated maximum salinity of applied water that sustains 100% yield of salt sensitive crops grown in the southern Delta (surface irrigation of mineral soils) per the University of California Guidelines and Irrigation Paper 29 of the Food and Agricultural Organization of the United Nations.

## Slide 3: Concern for Delta Water Salinity Levels
  Delta water quality important for agriculture even prior to the construction of:
The Central Valley Project -1944
The State Water Project – 1968
  Concern was salinity intrusion from the
  Pacific Ocean and the San Francisco Bay, particularly in dry years

## Slide 4: Prior to Construction of CVP and SWP
  During dry years, such as 1931, water with an EC of about 1.56 mmhos/cm extended into the southern Delta as far as the Grant Line Canal and Upper Roberts Island

## Slide 5: Control of Delta Salinity
  D-1275 and D-1291 were adopted in 1967 to, among other things, require the CVP and the SWP to control the salinity level in the Delta.

## Slide 6: Issue for SWRCB
  Issue in 1975
  What appropriate salinity level should be required to protect the beneficial use of water for the irrigation of Agricultural crops in the Delta?
  Predominant crops: (Beans, Corn and Alfalfa)

## Slide 7: Testimony Pertaining to Delta Agriculture – December 1976
Irrigation and Agronomy Experts from the University of California Agricultural Experiment Station testified
  Robert Ayers
  Roy Branson
  Franz Kegel
  Jewell Meyer

## Slide 8: Summary of UC Testimony (1)
  Irrigation water adds salt to soil
  Plants use water, leave salt
  Good farm management and water application practices are necessary
  Excess salt must be leached from soil
  Leached salt add salt to Delta water

## Slide 9: Summary of UC Testimony (2)
  Corn Studies on Peat Soils
  Difficult to farm under ideal conditions
  Generally below sea level
  Impossible to leach with sub- irrigation
  Difficult to leach with surface irrigation

## Slide 10: Summary of UC Testimony (3)
  Corn Studies on Mineral Soils
  Leaching fractions of 15% to 16% can be achieved with normal irrigations and winter precipitation
  Nine study locations during dry year (1976) found highest soil salinities and lowest apparent leaching fractions occurred where irrigation water was of highest quality (0.7 mmhos/cm)

## Slide 11: Terminology
  Salinity refers to total dissolved ionic solids (TDS) in water expressed in:
  parts per million (ppm),
  parts per thousand (ppt)
  milligrams per kilogram (mg/Kg)

## Slide 12: Terminology
  Electrical Conductivity (EC) is a measurement of the salinity of water where
  EC units are expressed in
  millimhos per centimeter (mmhos/cm) (old)
  deciSiemens per meter (dS/m) (new)
  mmhos/cm = dS/m
  uS/cm = 10dS/m

## Slide 13: Terminology
  EC of Irrigation Water (ECi, ECiw, ECw)
  EC of Soil Water (ECe, ECsw)
  EC of Drainage Water (ECd, ECdw)

## Slide 14: Summary of UC Testimony (4)
  Good leaching and low salt accumulations were found in all locations where the irrigation water supply averaged 1.1 mmhos/cm
  The wide variability in Delta soils contributed more to the variability in the salt accumulation than did the salinity of the water supply

## Slide 15: Summary of UC Testimony (5)
  Despite the above findings:
  UC Experts stated in December 1976
  “This study has shown that salinity is a problem now in the Delta. Given the wide variety of soils in the South Delta, good yields and diversity of crops appear to be related to water quality and levels of farm management”

## Slide 16: SWRCB Focus in Adopting D-1485
  It appears that in 1976 the SWRCB was most concerned with protecting crops grown on difficult to manage peat soils.
  The Board asked:
  “If the water quality guidelines, as presented in exhibit UC-1 and UC-2, need to be modified for use of subsurface irrigation as stated on page 8, line 26 and 27 of the UC-2 exhibit (FAO-29), can you suggest a way to modify?”

## Slide 17: UC Response
Mr. Ayers developed a four page answer that basically said:
  …in order to achieve a 100% corn yield on mineral soils using surface irrigation, a 16% leaching fraction with a water quality of 1.13 mmhos/cm would be needed.
  …in order to achieve a 100% corn yield on peat soils with subsurface irrigation a water quality of 0.42 to 0.85 mmhos/cm would be needed.

## Slide 18: SWRCB Adopted Water Quality Objectives for Agricultural Beneficial uses
  San Joaquin River at Airport Way Bridge,Vernalis
  Maximum 30-day running average of mean daily EC
  April – August: EC = 0.7 mmhos/cm
  September – March: EC = 1.0 mmhos/cm

## Slide 19: Salinity Research After D-1485 (1)
  Hoffman, et al (1983) reported on 3-year corn experiment in Delta and concluded
  “For subirrigation, an ECi up to 1.5 dS/m did not decrease yield as leaching had reduced ECsw below the threshold.
  “..surface irrigation with water of up to 6 dS/m after mid-season (end of July) did not reduce yield below that of treatments where the salinity of the irrigation water was not increased mid-season.”

## Slide 20: Salinity Research After D-1485 (2)
  Pritchard, et al (1983) reported
  “At the soil water salinity threshold of corn grain (3.7 dS/m), the average ratio is 1.7 which results in a maximum value of 2.2 dS/m of ECi without yield loss under normal conditions. With subirrigtion and below normal rainfall, as in 1981, the maximum value of ECi would be 0.8 dS/m”.

## Slide 21: Salinity Research After D-1485 (3)
  Isadoro-Ramerez, Berenguer-Merelo and Grattan (2004) reported
  “When and ECw of 1.1 dS/m is considered over the 53-year rainfall series (Davis) the model predicts that the seasonal mean ECe is 0.94 dS/m. In 80% of the years, the mean seasonal ECe is less than 1.0 dS/m, the yield threshold for salt-sensitive bean. For 50 of the 53 years, the seasonal mean ECe for individual years is 1.05 or lower, which would result in a predicted yield reduction of 1% or less. However, this predicted reduction in yield potential is less than the error associated with the yield threshold value itself.”

## Slide 22: Salinity Research After D-1485 (4)
  Isadoro-Ramerez, Berenguer-Merelo and Grattan (2004) summarized as follows:
  “Given these results, and taking into account all the other factors that potentially impact crop yield (e.g., weather, water stress, and biotic stresses) and the conservative nature of all inputs into the model, the use of 1.1dS/m as the threshold EC value for irrigation water is considered protective for beans, and thus all other agricultural uses of the water in the Davis area.”

## Slide 23: Southern Delta Service Area
  It is estimated that about 90% of the crops irrigated with San Joaquin River water in the Southern Delta are planted on mineral soils
  Beans most salt sensitive crop grown
  All beans are grown on mineral soils
  EC of 1.1 dS/m protective of beans and other crops grown with San Joaquin River water

## Slide 26: Conclusions
  Excellent crops are produced in the Southern Delta
  Farm management practices are more important than irrigation water salinity, within the range of Delta water quality, in regard to producing crop yields
  Even under the best circumstances, it is difficult to manage poor soils with a shallow water table
  Irrigation water with an EC = 1.1 dS/m is adequate to provide sustained 100% yield of salt sensitive crops grown in the southern Delta

## Slide 27: Recommended Water Quality Objectives for Agricultural Beneficial uses
  San Joaquin River at Airport Way Bridge,Vernalis
  Maximum 30-day running average of mean daily EC
  January - December: EC = 1.1 dS/m

## Slide 28: Methodology for Determining Compliance
  Change methodology to utilize the San Joaquin Basin 60-20-20 water year hydrologic classification index rather than the Sacramento River index.