## Slide 1
CALSIM II - San Joaquin River Basin
Refinements and Results
Presentation by Dan Steiner
On behalf of the San Joaquin River Group Authority
March 14, 2005

## Slide 2
Calaveras
Newman
Geographic Scope
New Melones
New Don Pedro
New Exchequer
Buchanan
Hidden
Millerton
New Hogan
River
Stanislaus
River
Tuolumne
River
Merced
River
Stevinson
Lander
Maze
Vernalis
Ripon
Modesto
Chowchilla
River
Fresno
River
San
Joaquin
River
San
Joaquin
River
Mendota Pool
Delta-Mendota Canal
California Aqueduct
Delta-Mendota Canal
California Aqueduct
San Luis Reservoir

## Slide 3: CALSIM II San Joaquin River Basin Enhancements
Revised hydrology
Land use based demands for Eastside water districts and adjacent areas
Improved system operating rules
Revised mapping of Westside and Eastside connectivity
Refinement / Addition of Friant and Calaveras systems
New formulation for calculation of water quality at Vernalis

## Slide 4: Revised Hydrology
Stream Accretions
  Mass balance approach using long-term gages
  Accounts for water entering and leaving stream reaches
  + Downstream Gage
  - Upstream Gage
  + Diversions
  - Return Flows
  + Runoff Adjustment
Resultant Value Represents
Precipitation runoff
Historical stream-groundwater interaction
Gage errors

## Slide 5: Representation of Land-use Based Demands Water Use Areas

## Slide 6: Representation of Land Use Based Demands Land Use

## Slide 7: Conceptual Area Water Balance Based on Land Use Demands
CUAW from CU model
Non-recoverable losses
Deep percolation
GW pumping
SW
Boundary
Returns to system

## Slide 8: Water Budgets and Representation of System Operations
Use historical land use to estimate consumptive use
Use historical operations data to perform water budgets
Results of water budgets are used to develop
Stream diversion requirements
Groundwater use parameters
District Operations
Approach varies depending on available data
Validation of system operations
Ensure model simulation depicts recent operations

## Slide 9: Representation of System Operations
Illustrative Example

## Slide 10: Validation of System Operations
New Don Pedro Operations

## Slide 11: Comprehensive San Joaquin River Basin Model
Calaveras
River
Stanislaus
River
Tuolumne
River
Merced
River
Chowchilla
River
Fresno
River
San Joaquin
River
Vernalis
Maze
Newman
Lander
Mendota Pool
San Joaquin River

## Slide 12: Comprehensive San Joaquin River Basin Model Simple Version Including Water Quality

## Slide 13: CALSIM II Current Conditions Test Simulation
CALSIM II fully integrated model logic, last modifications through January 2005.
Logic and results are currently under review with Reclamation
Represents current basin operations
    Decision 1641
    Decision 1422
    New Melones Interim Operations Plan
    San Joaquin River Agreement

## Slide 14: CALSIM II Current Conditions Test Simulation
First, results are presented for “Maze”, the San Joaquin River upstream of the Stanislaus confluence
    Captures the effects of upstream operations of the Merced River and Tuolumne River, and the occasional flow from the upper San Joaquin River and Kings River
    Water quality estimated with new CALSIM II mass balance approach
Results are then presented for “Vernalis”, as the conditions are affected by the Stanislaus River and the operation of New Melones
    Captures the effects of New Melones operating to the Interim Plan of Operation, sometimes specifically for Vernalis flow and quality objectives

## Slide 15: Simulation of San Joaquin River at Maze

## Slide 16: Simulation of San Joaquin River at Maze Comparison to Previous Modeling

## Slide 17: Simulation of San Joaquin River at Maze Comparison to Previous Modeling

## Slide 18: Simulation of San Joaquin River at Vernalis Stanislaus River Interim Plan of Operations

## Slide 19: Simulation of San Joaquin River at Vernalis Vernalis Objectives
The current water quality objective at Vernalis is a running 30-day
average of 700 uS/cm for April 1 through August 31, and 1000 uS/cm
for September 1 through March 31.
For the February through June non-pulse period (cfs):
October objectives

## Slide 20: Simulation of San Joaquin River at Vernalis New Melones Operations and Vernalis

## Slide 21: Simulation of San Joaquin River at Vernalis Vernalis Water Quality Compliance

## Slide 22: Simulation of San Joaquin River at Vernalis Vernalis Flow Compliance