## Slide 1: RECOMMENDATIONS OF THE SAN JOAQUIN RIVER GROUP AUTHORITY
SAN JOAQUIN RIVER FLOWS AIRPORT WAY BRIDGE, VERNALIS
FEBRUARY—APRIL 14 AND MAY 16—JUNE

## Slide 2: Questions Presented
Should the SWRCB amend the flow objectives for the San Joaquin River at Airport Way Bridge, Vernalis, for February through April 14 and May 16 through June in the Water Quality Objectives for Fish and Wildlife Beneficial uses (Table 3 of the 1995 Plan)? How should the objectives be modified and what are the scientific and legal arguments in support of and against modification?
Should the SWRCB change the methodology of determining the applicable San Joaquin River flow objectives that currently are determined by reference to the required Delta Outflow objective? How should the methodology for determining required flows be modified and what are the scientific and legal arguments in support of and against modification?

## Slide 3: February - April 14 and May 16 - June Flows
Lack of Sound Science
Based on Erroneous Assumptions
No Impacts to Salmon or Endangered Species
San Joaquin River’s Contribution to Delta Outflow

## Slide 4: Lack of Sound Science
SJR flows are identical to the flows in the Delta smelt biological opinion
SJR flows are just a fixed percentage of the required Delta outflows
SJR flows are highly influenced by Sacramento River conditions

## Slide 5
Year Type | Feb-June Flows (cfs)* | April-May Pulse Flows (cfs)*
C | 710-1,140 | 3,110-3,540
D | 1,420-2,280 | 4,020-4,880
BN | 1,420-2,280 | 4,620-5,480
AN | 2,130-3,420 | 5,730-7,020
W | 2,130-3,420 | 7,330-8,620

## Slide 6: San Joaquin River Flow as a Percentage of Delta Outflow
Water Year Type | % of Delta outflow | Min. Delta outflow (7,100 cfs) | X2 at Chipps Island (11,400 cfs)
C | 10% | 710 | 1,140
D | 20% | 1,420 | 2,280
BN | 20% | 1,420 | 2,280
AN | 30% | 2,130 | 3,420
W | 30% | 2,130 | 3,420

## Slide 7
 | Sacramento Valley |  |  | San Joaquin Valley |  | 
WY | WYsum | Index | Yr-type | WYsum | Index | Yr-type
1984 | 22.35 | 10.00 | W | 7.13 | 3.69 | AN
1985 | 11.04 | 6.47 | D | 3.60 | 2.40 | D
1986 | 25.83 | 9.96 | W | 9.50 | 4.31 | W
1987 | 9.27 | 5.86 | D | 2.08 | 1.86 | C
1988 | 9.23 | 4.65 | C | 2.48 | 1.48 | C
1989 | 14.82 | 6.13 | D | 3.56 | 1.96 | C
1990 | 9.26 | 4.81 | C | 2.46 | 1.51 | C
1991 | 8.44 | 4.21 | C | 3.20 | 1.96 | C
1992 | 8.87 | 4.06 | C | 2.58 | 1.56 | C
1993 | 22.21 | 8.54 | AN | 8.38 | 4.20 | W
1994 | 7.81 | 5.02 | C | 2.54 | 2.05 | C
1995 | 34.55 | 12.89 | W | 12.32 | 5.95 | W
1996 | 22.29 | 10.26 | W | 7.22 | 4.12 | W
1997 | 25.42 | 10.82 | W | 9.51 | 4.13 | W
1998 | 31.40 | 13.31 | W | 10.43 | 5.65 | W
1999 | 21.19 | 9.80 | W | 5.91 | 3.59 | AN
2000 | 18.90 | 8.94 | AN | 5.90 | 3.38 | AN
2001 | 9.81 | 5.76 | D | 3.18 | 2.20 | D
2002 | 14.60 | 6.35 | D | 4.06 | 2.34 | D
2003 | 19.18 | 8.18 | AN | 4.88 | 2.82 | BN
2004 | 16.05 | 7.50 | BN | 3.80 | 2.21 | D

## Slide 8
The Sacramento River Basin is primarily a rain-fed system, whereas the San Joaquin River Basin is a snow-fed system. This results in a significantly different runoff pattern which was recognized in the development and adoption of a separate index, the 60-20-20 index, for the San Joaquin system.
The unimpaired and impaired flows for the Sacramento River Basin are substantially greater than for the San Joaquin River Basin.
A substantial portion of the Sacramento River flows to the Delta for export, whereas most of the San Joaquin River is used within the basin or is exported out of the basin.
Water is imported into the Sacramento River Basin from the Trinity River, whereas water is exported out of the San Joaquin Basin.

## Slide 9: Salmon and Endangered Species
No correlation between San Joaquin River flow and Delta survival
San Joaquin River contributes little to Delta outflow
OCAP BO concluded no jeopardy

## Slide 12: May 16 to June Flows
Temperature
  Use of reservoir releases to control San Joaquin River temperature is a waste and unreasonable use of water
  Stanislaus River studies
  VAMP monitoring

## Slide 16: May 16 to June Flows
Most Salmon Smolts Have Left the System by late May
  Tributary rotary screw trap
  Mossdale trawl
  SWP and CVP salvage

## Slide 22: Proposed Vernalis Flow Objective
SJRBI | Vernalis Flow Objective (cfs) | 
 | NM Index < 2,500 TAF | NM Index > 2,500 TAF
1 — W | 2000 | 2500
2 — AN | 2000 | 2500
3 — BN | 1250 | 1750
4 — D | 1250 | 1750
5 — C | 700 | 1000